| BL2511SG |
| --- |
| Control System | Positive PWM control（1500 usec Neutral） |
| Operation Voltage Range | 4.8V ~6.0V |
| Operation Temperature Range | -20C°~ +60C° |
| Test Voltage: | At 4.8V | At 6.0V |
| Torque | 10kg.cm | 12kg.cm |
| Speed | 0.085sec / 60 deg | 0.074sec / 60 deg |
| Idle Current | 300mA | 350mA |
| Running Current | 2800mA | 3000mA |
| Dead band width | 1 usec |
| Circle | >15000 times/idle load |
| Operation Travel | 55°±5° |
| Direction | Anti-clockwise/ pulse travel 1500 to 2100 usec |
| Drive type | FET drive |
| Motor Type | Brushless |
| Potentiometer Type | Indirect |
| Amplifier Type | Digital |
| Dimensions | 40.8*20.2*26.1mm |
| Weight: | 62g （without accessories） |
| Ball Bearing | Double ball bearing |
| Gear Material | Import steal gear |
| Case Material | AL6061 |
| Connector Wire Length | 300mm |
| Connector Wire Gauge | 22AWG，JR universal |
| Brown | Negative |
| Red | Positive |
| Orange | Signal |
| Application | Car model；fixed-wing aircraft；helicopter |