| DC1611SG |
| --- |
| Control System | Positive PWM control（1500 usec Neutral） |
| Operation Voltage Range | 4.8V ~ 6.0V |
| Operation Temperature Range | -20C°~ +60C° |
| Test Voltage: | At 4.8V | At 6.0V |
| Torque | 20kg.cm | 22kg.cm |
| Idle speed | 0.163sec / 60 deg | 0.14sec / 60 deg |
| Idle current | 350mA | 400mA |
| Running Current | 3000mA | 3400mA |
| Death band width | 1 usec |
| Circle | >15000 times/ idle load |
| Operation travel | 55°±5° |
| Direction | Anti-clockwise/ Pulse Travel 1500 to 2100 usec |
| Drive type | FET drive |
| Motor type | Coreless |
| Potentiometer type | Indirect drive |
| Amplifier type | Digital |
| Size | 40*20*37.2mm |
| Weight | 53g （without accessories） |
| Ball bearing | Double ball bearing |
| Gear material | Import steel gear |
| Case material | Nylon plus fiber/ Aluminum medium |
| Connector Wire Length | 300mm |
| Connector Wire Gauge | 22AWG，JR Universal |
| Brown | Negative |
| Red | Positive |
| Orange | Signal |
| Application | Car model; fixed-wing aircraft; helicopter; robot. |
| GOTECK RC INC |  |  |