| DC2124TG |
| --- |
| Control System | Positive PWM control（1500 usec Neutral） |
| Operation Voltage Range | 4.8V ~6.0V |
| Operation Temperature Range | -20C°~ +60C° |
| Test Voltage: | At 4.8V | At 6.0V |
| Torque | 5.0kg.cm | 5.8kg.cm |
| Idle speed | 0.13sec / 60 deg | 0.12sec / 60 deg |
| Idle current | 200mA | 240mA |
| Running Current | 1600mA | 2000mA |
| Death band width | 1 usec |
| Circle | >15000 times/ idle load |
| Operation travel | 55°±5° |
| Direction | Anti-clockwise/ pulse travel 1500 to 2100 usec |
| Drive type | FET drive |
| Motor type | Coreless |
| Potentiometer type | Direct drive |
| Amplifier type | Digital |
| Size | 23*12*27.5mm |
| Weight | 20g （without accessories） |
| Ball bearing | Double ball bearing |
| Gear material | Import metal gear |
| Case material | AL6061 |
| Connector Wire Length | 180mm |
| Connector Wire Gauge | 26AWG，JR Universal |
| Brown | Negative |
| Red | Positive |
| Orange | Signal |
| Application | Car model；fixed-wing aircraft；helicopter |